HDMI TO COAX EXTENDER

User Manual

WolfPack HDMI Over Coaxial Extender

KISS YOUR HIGH DEFINITION PROBLEMS GOODBYE

HDTV Supply, Inc.

800-841-9238

www.hdtvsupply.com

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Please keep this manual for future reference.

The pictures and technical parameter involved are only for your reference, As for specific circumstances, please be subject to the actual product.

1.0 Introduction

With this HDMI to coax extender, HDMI signal can be transmitted over long distances via a single coaxial cable, which has extended transmission speed, uncompressed, zero latency, etc., can greatly reduce the cost of long-distance transmission of HDMI signal transmission distance of 100-300 meters.

2.0 Features

1. The interface operates at bit rates of 2.970 G bit/s, 2.970/1.001G bit/s, 1.485

G bit/s, 1.485/1.001G bit/s and 270 Mb/s.

2. Supports HDMI input timings: 480i@59.94, 576i, 720p@50/59.94/60,

1080i@50/59.94/60, 1080p@23.98/24/25/29.97/30/50/59.94/60.

3. HDMI TO COAX EXTENDER:

(3.1) 480i/576i to SD (SMPTE 259M-C, at bit rates of 270 M bit/s)

720p/1080i to HD (SMPTE 292M, at bit rates of 1.485 G bit/s or

1.485/1.001 G bit/s)

(3.2 )1080p to 3G (SMPTE 424M/425M-AB, at bit rates of 2.970 G bit/s

and 2.970/1.001 G bit/s)

4. SDI Extender supports distance between TX to RX:100 meters (3G),

200 meters (HD), or 300 meters (SD)

3.0 Package contents

Before attempting to use this unit, please check the packaging and make sure the following items are contained in the shipping carton:

HDMI Extender TX---------------------------------x1

HDMI Extender RX---------------------------------x1

5V1A DC Power Supply Adaptor---------------x2

Operation Manual-----------------------------------x1

4.0 Specifications

TX Input Port--------------------------------------------------------------------1 x HDMI

TX Output Port--------------------------------------1 x BNC (SDI/HD-SDI/3G-SDI)

RX Input Port----------------------------------------1 x BNC (SDI/HD-SDI/3G-SDI)

RX Output Port------------------------------------------------------------------1 x HDMI

Transmission Rates------------------2.970 G bit/s and 2.970/1.001 G bit/s

In/Output Resolution----480i, 576i, 720p@50/59.94,60 ,1080i@50/59.94/60

1080p@23.97/24/25/29.97/30/50/59.94/60

Power Supply-----------------------------------------------------------------------DC 5V

ESD Protection Human body model-------------------±8kV (air-gap discharge)

±4kV (contact discharge)

Dimension--------------------------------------------------82mm x 43.5mm x 23 mm

Weight-----------------------------------------------------------------------------------215g

Operating Temperature---------------------------------0°C ~ 40°C / 32°F ~ 104°F

Storage Temperature-----------------------------------20°C ~ 60°C / -4°F ~ 140°F

elative Humidity------------------------------------20 ~ 90% RH (Non-condensing)

Power Consumption (Max)--------------------------------------------------------- --5W

5.0 Panel descriptions

Please study the panel drawings below and become familiar with the signal

input(S) and output(S)and power requirements.

Transmitter Panel

HDMI INPUT-------------------------------HDMI input Interface

SDI OUPUT---------------------------------SDI output Interface

Status---------------------------------------Input Status Indicator

PW------------------------------------------------- Power Indicator

DC 5V------------------------------------------5V Power Interface

Receiver Panel

DC 5V-----------------------------------------5V Power Interface

PW------------------------------------------------- Power Indicator

Status---------------------------------------Input Status Indicator

SDI INPUT----------------------------------SDI output Interface

HDMI OUTPUT----------------------------HDMI input Interface

6.0 Installation and Operation

6.01Connect the HDMI cable between TX and HDMI Source;

6.02 Connect SDI cable between TX and RX;

6.03 Connect the HDMI cable to RX and HDMI terminal display;

6.04 TX and RX respectively connected to power adapter;

6.05 Open the HDMI source and HDMI display device power products began

to work.

7.0 INSTALLATION AND PRECAUTIONS

To avoid electric shock, product damage and to protect your safety, please notice the following:

- Please slowly plug or unplug signal cables and do not often plug, unplug, or shake them.

- 2.The equipment should not be placed under the sun, rain and damp or unventilated environment.

- Liquid items should not be placed on the equipment.

- Do not install the equipment near heat sources such as fire, power, or other amplifiers that produce heat.

- Do not insert the metal or other objects to the equipment in addition to connecting cables to ports.

- Do not demolish the equipment by yourself; it should be maintained by professional maintenance staff.

# What this WolfPack HDMI to Coax Converter Can & Cannot Do:

- CAN DO:

  - Convert an HDMI signal (like from a DVD player) to a coax cable AND CONVERT THE COAX CABLE BACK TO HDMI TO GO TO A TVs HDMI INPUT.

  - It will do nothing else.

  - Think of it as a long HDMI cable with HDMI connectors on both ends.

  - Both the Transmitter and Receiver MUST be used and each has an AC adapter.

- WHAT IT CANNOT DO:

  - Convert an HDMI signal to a coax signal to go into the coax input of a TV.

  - Convert a coax signal from the cable company to an HDMI signal.

  - Convert a coax signal from an antenna to an HDMI signal.

NOTE: In-house and existing passive splitters drop the signal strength in half, or more, so delete all the splitters and wire this device directly. This HDMI to Coax sends only one HDMI signal to a TV. It does not work any other way.