USER MANUAL

Table of Contents

1.0 Introduction........................................................................01

2.0 Features...............................................................................01

3.0 Specifications......................................................................02

4.0 Package Contents................................................................02

5.0 Panel Descriptions...............................................................03

6.0 Connection and Operation................................................03

2TOSLINK SPDIF+2COAXIAL to TOSLINK+L/R RCA+3.5mm Audio Switch Converter

Dear Customer

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Please keep this manual for future reference.

1.0 Introduction

This product is a 4-ports SPDIF Switcher, also is a digital to analog converter. You can switch any one of the four digital audio signals to the one SPDIF/TOSLINK audio output + one analog R/L output and one headphone output simultaneously. It works with the DVD、PS3、XBOX360、HD player、PC and other similar signal generator source.

2.0 Features

* 4-ports SPDIF(2xTOSLINK and 2xCOAXIAL)digital audio input, switch to 1-port SPDIF/TOSLINK output、one R/L analog audio and one headphone output

* Uses 192KHZ/24bit DAC

* Audio format support: LPCM, DTS, Dolby-AC3, THX, HDCD.

* Support LPCM digital audio converted to analog audio output

* Automatic identification input digital audio signal format, when non-LPCM input, analog output mute

* Support last time working state memory when power off

* Over-voltage protection can prevent the damage caused by connecting unmatched to the machine

* Input status indication. When no audio or error data input, the input port indicator starts to flash

* Headphone amplifier output, can drive the general 3.5mm earphone

* No loss of quality

* Installs in minutes

3.0 Specifications

| Analog Audio Output Support audio format | PCM/LPCM |
| --- | --- |
| Digital input level | 0.1~1Volts p-p |
| DAC sample frequency range | 32~192 KHz |
| DAC Bit rate range | 16-24 Bit |
| R/L output level（1KHz@0dB） | 1V RMS |
| Headphone output power(1KHz@0dB RL=32) | 30mW |
| SNR@0dB(CCIR/ARM) | 90dB |
| Distortion | 0.1% |
| Frequency response | 20Hz~20KHz |
| Max working current | 100mA |
| Operating Temperature range | (-10 to 55℃) |
| Operating Humidity range | 5 to 90％RH(No condensation) |
| Power Supply | 5V DC |
| Power Supply Cert | CE,FCC |
| AC Power Adapter | US standard、UK standard and so on |

Note: Specifications are subject to change without notice.

4.0 Package Contents

- Main Unit

- 5V DC Power Adapter

- User Manual

5.0 Panel Descriptions

6.0 Connection Diagram