USER MANUAL

Table of Contents

1.0 Introduction........................................................................01

2.0 Feature...............................................................................01

3.0 Specification......................................................................02

4.0 Package Content................................................................02

5.0 Panel Description...............................................................03

6.0 Connection and Operation................................................03

SDI 1X4 Splitter

Dear Customer

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Phase keep this manual for future reference

1.0 Introduction

This is a 1x4 SDI splitter, which make it possible to transfer 1SDI signal to 4 monitors simultaneously.Up to four outputs could save you lots trouble of setting other signals when you want to enjoy other SDI programs.

2.0 Feature

This product is specially designed with equalizer IC in its input and drive IC in its outputs.All of the input and outputs support long coaxial cable.

* Support multiple video resolution：

• SD 480i,576i and 625i

• HD 720p@24/25/30/ 50 / 60

• HD 1080i@50/60

• HD 1080p@24/25/30

• 3G 1080p@50/60

* Support multiple color space：

• RGB or YCbCr 4:4:4 sampled

• YCbCr 4:2:2 or 4:2:0 sampled

* Support wide range data rates：270Mbps～2.97Gbps.

* Support multiple deep color:8bit、10bit、12bit.

3.0 Specification

| Input Connector | 1x SDI BNC Male |
| --- | --- |
| Output Connector | 4x SDI BNC Male |
| Supported Cable Length (BELDEN 1694A) | 3G Mode: up to 100m |
|  | HD Mode: up to 200m |
|  | SD Mode: up to 400m |
| Limited Warranty | 1Year Parts and Labor |
| Operating Temperature | 0℃ to 70℃ |
| Operating Humidity | 10% to 85 % RH (no condensation) |
| Storage Temperature | -10℃ to +80℃ |
| Storage Humidity | 5% to 90% RH (no condensation) |
| Power Supply | 5V DC@2A |
| Power consumption(MAX) | 1.2W |
| Splitter Unit Cert | FCC.CE, RoHS |
| Power Supply Cert | CE,FCC, RoHS |
| User Manual | English Version |

Note: Specification is subject to change without notice.

4.0 Package Content

1) Main unit

2) Power adapter 5V@2A

3) User Manual

5.0 Panel Description

6.0 Connection and Operation

6.1 Connection

(1) Connect the product to appropriate power;

(2) Connect the SDI signal to the“IN” through 75Ωcoaxial cable of high quality（BELDEN 1694 A cable or equivalents as well）;

(3) Connect the SDI monitor or other SDI devices to the“OUT1”（ “OUT2”、“OUT3” 、“OUT4”）through 75Ω coaxial cable.

(4)Operate the SDI signal to start the show.

6.2 Connection Diagram