USER MANUAL

Table of Contents

1.0 Introduction.........................................................................01

2.0 Feature.................................................................................01

3.0 Specification.......................................................................02

4.0 Package Content................................................................02

5.0 Panel Description................................................................03

6.0 Connection and Operation.................................................03

AHD to HDMI +AHD /CVBS/VGA/YPbPr Converter W/Scaler (720P/1080P)

Dear Customer

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Please keep this manual for future reference.

- Introduction

This converter can convert one channel AHD input to one channel HDMI/CVBS/VGA/YPbPr outputs, and one channel AHD looping output .The device comes with a scaler that will allow you to adjust the output signal to 720p/1080p that is compatible your HDMI/VGA/YPbPr-enabled display, and 480i(NTSC) or 576i(PAL) for CVBS output. The converter helps reduce equipment cost by eliminating the need to convert to each individual analog component, by offering a solution that converts AHD source for use with multiple displays. For hassle-free installation, it offers a plug-and-play solution that requires no software or driver installation.

2.0 Feature

* Input: 1 x AHD

* Output: 1 x AHD, 1 x HDMI, 1 x CVBS, 1 x VGA, 1 x YPbPr

* The HDMI/CVBS/VGA/YPbPr output is selected by the ‘switch’ button, only one port can output the video each time.

* Support highest resolution at 1080p@60Hz for HDMI/VGA/YPbPr output, and 480i/576i for CVBS output.

* No need to install drivers, portable, flexible, plug and play.

* Coaxial cable impedance: 75Ω

* Support AHD loop output

* Support AHD signal transmission distance up to 500m

* Support wide range voltage for power adapter: 5V~12V

3.0 Specification

| Input Signal | AHD Signal |
| --- | --- |
| Output Signal | AHD x1,HDMI x1, CVBS x1,VGA x1,YPbPr x1 |
| AHD Input Resolution | 720p@25Hz/30Hz,720p@50Hz/60Hz,1080p@25Hz/30Hz |
| AHD Output Resolution | 720p@25Hz/30Hz,720p@50Hz/60Hz,1080p@25Hz/30Hz |
| HDMI Output Resolution | 720p@60Hz,1080p@60Hz |
| VGA Output Resolution | 1280x720@60Hz,1920x1080@60Hz |
| CVBS Output Resolution | 576i(PAL) and 480i(NTSC) |
| YPbPr Output Resolution | 720p@60Hz,1080p@60Hz |
| Limited Warranty | 1 Year Parts and Labor |
| Operating Temperature | -40℃ to +120℃ |
| Operating Humidity | 10% to 85 % RH (no condensation) |
| Storage Temperature | -30℃ to +50℃ |
| Storage Humidity | 5% to 90 % RH (no condensation) |
| Power Supply | 5V~12V DC |
| Power Consumption (Max) | 5W |
| Converter Unit Cert. | FCC,CE, RoHS |
| User Manual | English Version |

Note: Specification is subject to change without notice.

4.0 Package Content

1) Main Unit

2) 5V DC Power Adapter

3) User Manual

5.0 Panel Description

6.0 Connection and Operation