U S E R   M A N U A L

1X2 HDMI 2.0 splitter 4K

(HDMI 2.0,HDCP2.2 ,4K,IR extension, EDID management, RS232)

Enjoy the vivid world !

INTRODUCTION

The 1x2 HDMI Splitter uses a single HDMI source,accessing to multiple HDMI sinks. It allows one HDMI device to be split easily to 2 HDMI compatible monitors or projectors. In addition，it can be placed at the end of a long HDMI cable to regenerate the HDMI signal. The resolution of this hdmi splitter can be up to 3840X2160/60Hz.

This product can support EDID management function, comes with eight kinds of EDID mode, the users can choose according to their own needs. In addition, it is with built-in IR extension function, it can work with our hdmi 2.0 repeater which has IR-RX to receive the IR command to control the source.

FEATURES

- Support HDMI 2.0 ,HDCP2.2

- Support 3D video format

- Support high resolution up to 3840X2160/60HZ

- Support the max baud rate of 6G and TMDS clock can be up to 600 MHz

- Support  8/10/12 bit deep color

- Support AWG26 HDMI standard cable:

when the resolution is 1080p and below, input up to 8 meters,output to 8 meters.

when the resolution is 4K, input up to 8 meters, output up to 8 meters.

- Support single HDMI source，accessing to multiple HDMI sinks, the source can be DVD player, A/V receiver, set top box and etc.

- Built-in IR extension function.( it can work with our hdmi 2.0 repeater which has IR-RX to receive the IR command to remote control the source)

- Support serial port online upgrade

- Support EDID management

- 5V/2A power adapter

Specifications:

HDMI version  ………………………………………………………………………………. HDMI 2.0

HDCP version  ……………………………………….……………………………………. HDCP 2.2

HDMI resolution ……………………………….. ……….. ……….. …………up to 3840*2160/60Hz

Support video format ………………………………..…………………………8/10/12bit Deep color

Support audio format………………..………. …….DTS-HD/Dolby-trueHD/DTS/Dolby-AC3/DSD

Max bandwidth………………………………………………………………………………….600MHz

Max baud rate……………….…….………………….…………………………………………..6Gbps

Input cable distance.…………………………….(1080p resolution) ≤8m,(4K resolution)≤8m AWG26 HDMI standard cable

Output cable distance…………………………(1080p resolution) ≤8m,(4K resolution)≤8m AWG26 HDMI standard cable

Max working current………………………………………………………………………………....1 A

Power adapter format………………….….input AC (50Hz, 60Hz) 100V-240V; output: DC5V/2A

Operating Temperature range……………………………..…………….………………(-15 to +55℃)

Dimension (L x W x H)………………...............…………..……………………….154x60x24 (mm)

Weight…….…..………………………………………………………..…….……………………335g

Product interface pictures

①：5V Power Interface

②：Power adapter indicator

③：HDMI output port

④：LED Output indicator

⑤：HDMI input port

：LED Input Indicator

⑦：RS232 port ,serial port online upgrade

⑧：IR TX Extension Interface

⑨：DIP switch，using for EDID management

⑩：Power switch

DIP EDID Switch Description：

DIP 1   2   3   4
         X  0   0  0    ：copy output1 EDID only
       X  0   0    1    :  EDID MIX
          X  0   1    0    :  EDID Download (RS232)
          X  0   1    1    : 4K X 2K  30Hz
          X  1   0    0    : 4K X 2K  60Hz
          X  1   0    1    : 1080P 3D 2ch
          X  1   1    0    : 1080P 2D 2ch
          X  1   1    1    : 1080P 2D 5.1ch

1 is used for upgrades, 1 is upgrading mode, 0 is normal working mode (switch down is 1, otherwise is 0)

Working Mode Description：

There are two working mode for product, normal working mode and upgrading mode, which is decided by DIP EDID switch 1, 1 is upgrading mode，0 is normal working mode.

IR Extension description:

There is an IR TX Extension port, it can work with an optional HDMI 2.0 repeater which works as IR-RX and IR extended via HDMI cable

Output port:

Only output1 can support CEC function, output 2 support IR extension function.

Connection and Operation:

1: connect the HD source to the splitter input with one hdmi cable

2: connect the splitter output to the diaplays with 2 hdmi cables

3: connect 5V/2A power adapter to the splitter

Package include :

1. HDMI splitter       x1pc

2. Power adapter      x1pc

3. User manual       x1pc

4. IR cable           x1pair

5. HDMI repeater (optional)