Hi Resolution Video to VGA Converter

ITEM NO.: AD001HH High Resolution Video to VGA Converter with HDMI output

Features:

- Special designed for computer VGA/ HDMI monitor, LCD color monitor.

- Input: composite video input via RCA, Output: Video(CVBS), VGA ,HDMI output

- Support NTSC, PAL video system.

- Input video system 50 to 60Hz frame rate detection (NTSC/PAL).

- Support VGA, HDMI resolution: 800x600、1024x768、1280x720、1920x1080@60Hz。

- Support HDMI output: 720P、1080I、1080P

- Built in stereo audio input and output.

- Any adjustment will be auto memory.

- Frequency output:  60Hz, 75Hz, 85Hz.

- On screen display function: Resolution、Brightness、Contrast、Saturation、Hue.

Operation Controls and Function:

Button Function:

MENU	： OSD ON/OFF。

UP		： Select up or Increase setting value

DOWN	： Select down or Increase setting value

SELECT	： Select or setting.

OSD Menu：

  - Resolution

Press  SELECT button to setup resolution:  800x600、1024x768、1280x720、1920x1080

  - Brightness

Press  UP  or DOWN button to decrease/increase from 0 ~100。

  - Contrast

Press  UP  or DOWN button to decrease/increase from 0 ~100。

  - Saturation

Press  UP  or DOWN button to decrease/increase from 0 ~100。

  - Hue

Press  UP  or DOWN button to decrease/increase from 0 ~100。

Factory Default value setting：

Resolution	800 x 600

Brightness	50

Contrast		50

Saturation	50

Hue			50

NOTE: Wrong Resolution setting will cause the picture not display, please initialize factory default value.

Remark:

1. Under OSD mode: OSD will be auto save after setup and turn off OSD mode after 10 seconds.

2. OSD function only display on VGA, HDMI output mode.

3. Initialize factory default: Unplug the power adaptor, then press MENU button and plug the power adaptor until LED blinking, then release MENU button.

View of Connection and Installation:

Panel View:

Specification:

| ITEM | AD001HH |
| --- | --- |
| Resolution | Up to 1920 x 1080 non-interlaced to 60Hz |
| Composite Video | RCA Input/Output x 2 |
| Stereo Audio | RCA Input/Output x 4，PHONE JACK 3.5mm x 1 |
| VGA Connector | 15-pin Mini D-sub (High Density) x 1 |
| HDMI Connector | HDMI x 1 |
| Function Button | Button x 4 |
| Function Adjust | Resolution、Brightness、Contrast、Saturation、Hue |
| Power Supply | 5V DC．2000mA Regulated ( External ) |
| Power Consumption | 1100 mA ( max ) |
| Dimensions W x H x D mm | 140 x 96.5 x 32 (mm) |
| Weight g | 350 g |