HDMI Video Distribution Amplifier

ITEM NO.:  HD02, HD04

HD02, H04 is a distribution amplifier for HDMI signals. Both of them built in 2 input selection for variety application.  It reclocks and equalizes the signal and distributes it to two, four identical outputs.

HD02   2 Input 2 Output HDMI Distribution Amplifier

- Connects up to 2 HDMI displays at the same time from a digital video source.

- 2 input selectable by front buttons (A/B).

- A, B Input could be setup by auto jump or manual setting.

- Support high resolution: 480i、480p、720p、1080i、1080p @24/50/60Hz

- Bandwidth: 25-225Mhz, support up to 12-Bit deep color.

- Support DTS-HD、Dolby True HD、LPCM 7.1

- Support HDCP 1.3a, HDCP compliant.

HD04  1 Input 4 Output HDMI Distribution Amplifier

- Identical to HD02, but 4 HDMI displays at the same time from a digital video source.

Panel View:

HD02

HD04

Installation View:

- Connect HDMI source to HDMI splitter Input A or B input，Output 1~4 to monitor.

- Output 1 as EDID Master Port.  Recommend connect all HDMI equipments first, then power on, it will auto copy Master Port EDID for HDMI source reference which take around 10 seconds.

- Input A、B by front button selection.

- Input LED flash:  no any signal detected.

- Press A, B buttons together to activated/disabled auto jump function.

6. Auto Jump function ON:  A, B  Blue LED flash at same time.

7. Auto Jump function OFF:   A, B  Blue LED on at same time.

LED Indication:

POWER ON/OFF 	Green

INPUT A			Blue

INPUT B			Blue

OUTPUT 1			Blue

OUTPUT 2			Blue

OUTPUT 3			Blue

OUTPUT 4			Blue

Remark：

1. There are some DVD equipments still have +5V signal output under power off status, it will cause auto jump function abnormal, please disable auto jump and setup by press A, B button to avoid any abnormal operation.

2. HD02/H04 no memory function, it will back to factory default once power off. (input A , auto jump function off)

Specification:

| ITEM NO. | HD02 | HD04 |
| --- | --- | --- |
| Resolution | 480i/p、720p、1080i/p @24/50/60Hz |
| HDMI Connector | Input: 2 port (HDMI Type A), Output: 2 port ( HDMI Type A) | Input: 2 port (HDMI Type A), Output: 4 port ( HDMI Type A) |
| A / B input | Button switch x 2 |
| Supports Bandwidth | 25-225Mhz, support up to 12-Bit deep color |
| Supports Resolution | 480i,576i,480p,720p,1080i,1080p |
| Operation Temperature | -10℃~45℃ |
| Storage Temperature | -30℃~70℃ |
| Power Consumption | 1500mA (Max) | 1500mA (Max) |
| Power Supply | DC5V2AMP |
| DIMENSIONS W x H x D mm | 167 x 96 x 40 (mm) | 253 x 138.5 x 40 (mm) |
| Weight | 450 g | 800g |