PC Remote Control Device

ITEM NO.:  RC01

RC01  RS232 to UART Converter

- RS232 to UART converter terminal device

- To add this converter terminal for PC Remote control option with SHETECH switcher series product.

- Application for model number: CS04M, YS04M,HS04, HS07.

Installation View:

4 PIN convert 5 PIN Console Link Define：

▼                                        ▼

Specification:

| ITEM | RC01 |
| --- | --- |
| PC (RS-232) | DB9 Connector (Female) |
| Console (CS04M,YS04M, HS04,HS07) | 4 PIN Female Header |
| Distance | 15M (max) |
| Baud Rate | 115200 bps (max) |
| Power Source (DC) | From Terminal +5V |
| Power Consumption | 50 mA (max) |
| Dimension W×H×D mm | 57.5 × 33.5 × 16.5 (mm) |
| Weight g | 25 g |

# Text boxes

YS04M

CS04M

HS04,HS07

,

H

Console cable

RC01

RS-232

PC

GND

RX

TX

+5V

| 供電方式 | 由Terminal供應 +5V |
| --- | --- |
| 耗電流 |  |

GND

RX

TX

+5V

KEY