HDTVDA0102DSA User Manual

1x2 HDMI Splitter Scaler

Thank you for purchasing this product. For optimum performance and safety, please read these instructions carefully before connecting, operating or adjusting this product. Please keep this manual for future reference.

SURGE PROTECTION DEVICE RECOMMENDED

This product contains sensitive electrical components that may be damaged by electrical spikes, surges, electric shock, lightning strikes, etc. Use of surge protection systems is highly recommended in order to protect and extend the life of your equipment.

Table of Contents

- Introduction.............................................................................................4

- Features.....................................................................................................4

- Panel Descriptions.........................................................................................................5

- Application Diagram...........................................................................................................7

- Specifications..........................................................................................................7

- Package Contents.......................................................................................8

- Maintenance................................................................................................................8

- Warranty Policy.......................................................................................................8

- Limitations of Warranty.........................................................................................8

- Exclusive Remedies........................................................................................9

- RMA Policy...........................................................................................9

Introduction:

HDTV Supplys WolfPack 1x2 HDMI Splitter Scaler is designed to downscale a 4K2K signal to 1080p@60/50Hz or upscale a low resolution signal to 1080P@60/50Hz. The device features a single HDMI input and two simultaneous HDMI outputs, a 'Bypass' output and a 'Scaling' output. The Bypass output will always bypass the original signal, while the Scaling output will always downscale or upscale the original signal to 1080p. The HDMI 4K2K Splitter Scaler is an ideal solution for integrating a 4K2K source into a 1080p HD system.

Features:

- Supports HDMI signal downscaling from 4K2K to 1080p or upscaling from low resolution to 1080p

- Supports HD resolutions of 1080p@60/50Hz

- Supports 4K2K resolutions of 4096×2160p@24Hz and 3840×2160p@24/25/30Hz

- Supports audio extract for both SPDIF and L/R outputs.

- Supports EDID management

- Simultaneous HDMI output

Panel Descriptions

Front Panel

- Input LED indicator ---Indicate the status of the input for the unit.

- Power LED indicator---Indicate the status of the power for the unit.

- Output LED indicators --- Indicate the status of the outputs for the unit.

Back Panel

- HDMI input--- Connect to a HDMI source device such as Blu-ray/DVD player.

- HDMI output 1--- Bypass: Connect to a HDMI equipped TV/display to display the bypass output. Output resolution will depend on the original input signal.

- HDMI output 2--- Scaling: Connect to a HDMI equipped TV/display to display the scaling output. Output resolution will be fixed on 1080P@60/50Hz.

1) If the input resolution is 480i/576i/480P/720P/1080i, then it upscales to 1080P.

2) If the input resolution is 1080P, then it keeps 1080P.

3) If the input resolution is 4K2K, then it downscales to 1080P.

- Coaxial audio out--- RCA connector, extract audio from HDMI input.

- L/R audio out--- 3.5mm stereo phone-jack, extract audio from HDMI input, will mute if multichannel audio.

- Power port--- Connect the 5V DC power supply to the unit and plug the adaptor into an AC outlet.

Side Panel

- DIP switcher---For EDID management.

[DIP]=0000: Copy EDID From Output1, i.e., EDID pass through

[DIP]=0001: HDMI 1080p@60Hz, Audio 2CH PCM

[DIP]=0010: HDMI 1080p@60Hz, Audio 5.1CH PCM/DTS/DOLBY

[DIP]=0011: HDMI 1080p@60Hz, Audio 7.1CH PCM/DTS/DOLBY/HD

[DIP]=0100: HDMI 1080i@60Hz, Audio 2CH PCM

[DIP]=0101: HDMI 1080i@60Hz, Audio 5.1CH PCM/DTS/DOLBY

[DIP]=0110: HDMI 1080i@60Hz, Audio 7.1CH PCM/DTS/DOLBY/HD

[DIP]=0111: HDMI 1080p@60Hz/3D, Audio 2CH PCM

[DIP]=1000: HDMI 1080p@60Hz/3D, Audio 5.1CH PCM/DTS/DOLBY

[DIP]=1001: HDMI 1080p@60Hz/3D, Audio 7.1CH PCM/DTS/DOLBY/HD

[DIP]=1010: HDMI 4K2K, Audio 2CH PCM

[DIP]=1011: HDMI 4K2K, Audio 5.1CH PCM/DTS/DOLBY

[DIP]=1100: HDMI 4K2K, Audio 7.1CH PCM/DTS/DOLBY/HD

[DIP]=1101: DVI 1280x1024@60Hz, Audio None

[DIP]=1110: DVI 1920x1080@60Hz, Audio None

[DIP]=1111: DVI 1920x1200@60Hz, Audio None

Application Diagram

Specifications

| Bandwidth | 2.97Gbps per color |
| --- | --- |
| Video Input Connectors | 1x HDMI Type A, 19-pin, female |
| Video Output Connectors | 2x HDMI Type A, 19-pin, female |
| Audio Output Connectors | 1x RCA(SPDIF), 1x 3.5mm stereo jack (L/R) |
| EDID | 4-PIN DIP Switch |
| Mounting kit | Mounting ears included |
| Dimensions (W x D x H) | 150mm x 70mm x 23mm, without feet |
| Shipping Weight | 0.3KG |
| Operating Temperature | 32°F to 104°F (0°C to 40°C) |
| Storage Temperature | - 4°F to 140°F (- 20°C to 60°C) |
| Power Supply | 5V/2A DC |

Package Contents:

  - 1 - HDTVDA0102DSA

  - 1 - 5V/2A DC power supply

  - 1 - Mounting kit.

Maintenance

Clean this unit with a soft, dry cloth. Never use alcohol, paint thinner or benzene to clean this unit.

Warranty Policy

HDTV Supply products are warranted against defects in material and workmanship for one year from the date of shipment. During the warranty period, HDTV Supply will, at its option, repair or replace products that prove to be defective. Repairs are warranted for the remainder of the original warranty or a 90-day extended warranty, whichever is longer.

For equipment under warranty, the owner is responsible for freight to HDTV Supply and all related customs, taxes, tariffs, insurance, etc. HDTV Supply is responsible for the freight charges only for return of the equipment from the factory to the owner.

All equipment returned for warranty repair must have a valid RMA number issued prior to return and be marked clearly on the return packaging. HDTV Supply strongly recommends all equipment be returned in its original packaging.

HDTV Supplys obligations under this warranty are limited to repair or replacement of failed parts, and the return shipment to the buyer of the repaired or replaced parts.

Limitations of Warranty

The warranty does not apply to any part of a product that has been installed, altered, repaired, or misused in any way that, in the opinion of HDTV Supply, would affect the reliability or detracts from the performance of any part of the product, or is damaged as the result of use in a way or with equipment that had not been previously approved by HDTV Supply.

The warranty does not apply to any product or parts thereof where the serial number or the serial number of any of its parts has been altered, defaced, or removed.

The warranty does not cover damage or loss incurred in transportation of the product.

The warranty does not cover replacement or repair necessitated by loss or damage from any cause beyond the control of HDTV Supply, such as lightning or other natural and weather related events or wartime environments.

The warranty does not cover any labor involved in the removal and or reinstallation of warranted equipment or parts on site, or any labor required to diagnose the necessity for repair or replacement.

The warranty excludes any responsibility by HDTV Supply for incidental or consequential damages arising from the use of the equipment or products, or for any inability to use them either separate from or in combination with any other equipment or products.

A fixed charge established for each product will be imposed for all equipment returned for warranty repair where HDTV Supply cannot identify the cause of the reported failure.

Exclusive Remedies

HDTV Supplys warranty, as stated is in lieu of all other warranties, expressed, implied, or statutory, including those of merchantability and fitness for a particular purpose. The buyer shall pass on to any purchaser, lessee, or other user of HDTV Supplys products, the aforementioned warranty, and shall indemnify and hold harmless HDTV Supply from any claims or liability of such purchaser, lessee, or user based upon allegations that the buyer, its agents, or employees have made additional warranties or representations as to product preference or use.

The remedies provided herein are the buyer’s sole and exclusive remedies.  HDTV Supply shall not be liable for any direct, indirect, special, incidental, or consequential damages, whether based on contract, tort, or any other legal theory.

RMA Policy

When returning product to HDTV Supply for any reason, the customer should fill out the official RMA form to obtain a RMA number. Without the permission or approval, HDTV Supply will be no responsible for any return.

This can be initiated by emailing or calling your related sales.

All requests are processed within 48 hours.

Standard Replacement

For customers that agree to return defective product to HDTV Supply first, a Standard Replacement option is available.

An RMA number must first be issued by sales. This RMA number will need to be referenced on the outside of the return shipment.

Upon receipt of the defective product, HDTV Supply will, at its discretion, either repair or replace the product and ship it out in the most expeditious manner possible. Subject to availability, the replacement product will be shipped on the business day following receipt of the defective product.

In the event the product returned to HDTV Supply has been discontinued (i.e. the product is no longer being manufactured by HDTV Supply but is still under warranty), HDTV Supply will, at its discretion, either repair or replace with recertified product.

Once you have obtained an RMA number

After obtaining an RMA number from HDTV Supply, you must send the product - freight prepaid - to HDTV Supply. The HDTV Supply RMA number must be prominently displayed on the outside of your package. If you send your product to HDTV Supply without the RMA number prominently displayed on the outside of the package, it will be returned to you unopened.

Please use a shipping company that can demonstrate proof of delivery. HDTV Supply does not accept responsibility for any lost shipments unless proof of delivery to HDTV Supply is provided.

Please note:

Product shipped to HDTV Supply must be properly packaged to prevent loss or damage in transit.

Shipping your RMA to HDTV Supply using regular mailing envelopes is not acceptable, as they do not protect the product from damage during shipping.

HDTV Supply will not repair or replace a module that is shipped in such a way that the product is not properly protected.

HDTV Supply will not accept any product that has been damaged as a result of accident, abuse, misuse, natural or personal disaster, or any unauthorized disassemble, repair or modification.