SDI/ASI Matrix

We could do 144X144 mixed matrix for SDI/HDMI/DVI/VGA/Ypbpr/CVBS

XIT

Specifications

| Category | SDI Matrix Switcher |
| --- | --- |
| SDI Video |
| Application standard | SMPTE424M,SMPTE295M,SMPTE292M,ITU-R BT.601,ITU-R BT.1120 |
| Video format | 270Mbps SDI,1.485Gbps HD-SDI & 2.97Gbps 3G-SDI |
| Data frequency | 19Mbps to 2.97Gbps |
| Range | 0.8Vp-p±10% |
| Rise/fall time | ＜270ps |
| DC excursion | 0v±0.5v |
| Overshoot | <10% |
| Shift | <540ps±10% |
| Min/max electricity frequency | 0.5V to 1.0Vp-p |
| Max transmission range | 3G: 120m. HD: 200m SD:400m(use 75-5,128 professional video line,or 75-5 closed circuit television line, far transmit distance and low cost |
| Input impedance | 75Ω |
| Return loss | <-15dB, DC@1MHz to 1.5 GHz |
| DC compensation | Max ±5mV |
| Output impedance | 75Ω |
| RS-232 control interface |
| Serial control interface | RS-232, 9-pin female D-type interface |
| Baud rate and protocol | Baud rate: 9600, data bit:8, stop bit: 1, no parity |
| Structure of serial control interface | 2 = TX, 3 = RX, 5 = GND |
| Working Environment |
| Power supply | 100VAC~240VAC, 50/60 Hz, international adaptive power |
| Temperature | Storage and operating temperature: -40°~ +70°C |
| Humidity | Storage and operating humidity: 10% ~ 90% |
| MTBF | 60,000 hours |

# Text boxes

Data Sheet

Description

SDI Video Matrix Switcher is a professional matrix switcher of high-performance embedded intelligent control. Our SDI is compatible with ASI which is used widely in broadcasting program transmission.  It provides a stable and reliable high-definition audio and video signal transmission switching hub for the system. It is widely applied in digital video multi-screen display systems, radio and television systems, multimedia video conference, large screen display systems, high definition television teaching, visual command and control centers, medical teaching, etc

Features

- Compatible with SMPTE259M/292M/344M/424M , DVB-ASI

- Support clock recovery

- Built in self-adaptable equalize

- Power off self-protection

- High-quality, high-volume production, high compatibility and stability, and highly cost effective;

- Front panel LED shows  switching status

- Switching mode: RS-232, panel buttons, NET(optional)

- Rack mount design for easy installation

Ordering Information

| Mode | Specification |
| --- | --- |
| FL416S | 4input 16output SDI matrix |
| FL816S | 8input 16output SDI matrix |
| FL1616S | 16input 16 output SDI matrix |
| FL3232S | 32input 32output SDI matrix |

Note: we could not list every model of such flexible equipment, so just inform me your requirement; our sales will give more information to serve.