Ⅰ. Introduction

This Composite to HDMI Scaler takes either Composite Video or S-Video as input and converts it to HDMI. It allows older analog devices to be integrated into today's home theater system.

II. Features

1. Scales up Composite Video or s-video to HDMI 1080p;

2. Motion Compensated 3D Wavelet Video Coding Technology is applied to make the converted picture rich in color and more vivid;

3. Input audio is integrated into HDMI out as well as pass-through to earphone or sound box output;

4. Input video systems - NTSC and PAL is automatically detected and adjusted.

III. Operation Controls and Functions

①S-VIDEO IN:  S-VIDEO input

②VIDEO IN, AUDIO/R IN and AUDIO/L IN: Composite video and Audio L/R Input;

③DC 5V: To connect DC 5V power supply;

④POWER: Power LED;

⑤SWITCH: Select Composite Video or S-VIDEO input.

⑥AUDIO OUT: To connect earphone or sound box;

⑦HDMI OUT: To connect HD display.

IV. Specifications

1. Input:

One Composite Video,

One AUDIO L/R,

One S-video

2. Output:

One HDMI;

One Audio;

3. Power:

DC 5V/2A

4. Dimension: 74.5(W)×1148(L)×128(H)mm

5. Net Weight: 0.30kg

V. Connection Image:

Box Contents:

1pcs Composite video and s-video to HDMI converter

1pcs Power supply

1pcs User Manual

Composite and S-video to HDMI Converter

USER MANUAL