1 in 3HDMI 1 in 3 out CAT5 Extender with Chainable Receiver

ITEM NO.:  HE03L

- Extends HDMI signal over one CAT5/5e/6 cable.

- Including HE03LT transmitter and HE03LR receiver unit.

- Receiver built in 1 x HDMI output and 2 x CAT5 output for chainable to another receiver

for longer distance and multiple displays.

- HE03LR receiver could be chainable up to 31 layers with distance 3.1KM.  It also could

be cascade, total up to 100 displays

- HDMI 1.3 compliant.

- HDCP compatible.

- Transmission range up to 100M at 1080p.

- Plug and play for easy operation.

Installation view:

Panel view:

HE03LT

HE03LR

Cable:

Video Link cable using high quality CAT5E UTP/STP/FTP or CAT6 UTP cable.

RJ45 Define:

Link Cable ( TIA/EIA-568-B )

1. Orange-white		Data 1 +

2. Orange		   	     Data 1 -

3. Green-white		     Data 2 +

4. Blue				Data 3 +

5. Blue-white			Data 3 -

6. Green				Data 2 -

7. Brown-white		Data 4 +

8. Brown				Data 4 -

LED Indication Status:

Power	    On   ( power )

Link          Flash ( under linking )

On   ( linking )

RJ-45 Define:

Green        Flash ( Data transmission )

Orange       On   ( linking )

Caution:

The cabling must away from any equipment with electromagnetic wave, i.e.: microwave, radio equipment, high voltage.

Specification:

| ITEM NO. | HE03LT | HE03LR |
| --- | --- | --- |
| Support Resolution | Up to 1920 x 1080 |
| Transmission Distance | 100M (Max) |
| HDMI Connector | A-Type x 1 | A-Type x 1 |
| RJ45 Connector | RJ45 x 1 | RJ45 x 3 |
| Power Supply | DC5V 2Amp | DC5V 2Amp |
| Power Consumption | 860mA | 950mA |
| Temperature | Operation: 0 to 55℃, Storage: -20 TO 85℃, Humidity: up to 95% |
| Dimensions W x H x D mm | 67*140*27 (mm) | 67*155*27 (mm) |
| Weight g | 220 g | 250 g |