RS232 Protocol

ASCII Command [terminal command]

All command must Carrier Return (0x0d)

>>VR + CR    // Version command

8x8H_FW_01_02  (show version number 01.02

>> Single Output Set

I*>O?   // input * to output ?

I* can be from 0 to 8

0 for turn off

O? can be from 1 to 8 (port 1 to 8)

Or A for All Output port

Example:

I1>O2 // intput 1 to output2

I0>O2 // set output2 off

>> Multi Output Set

I*>O?,&,%...+CR   // input 1 to multi output

I* can be from 0 to 8

0 for turn off

O?,&,%. can be from 1 to 8 and separate by ‘,’

I3>O1,3,5,7

Set Input3 to output 1,3,5,7

>>MAP		// show 8 output port mapping

O1I3

02I4

03I0

04I4

05I3

06I1

07I2

08I3

>>EDRP?				// Read EDID from hdmi port ?

EDRP1 read EDID value from port 1

>>EDRI?				// Read Source EDID?

EDRI1 read Input source 1EDID value

>> EDLP?*				// Learn EDID from port ? to source *

?: HDMI port number 1~8

*: Input. 1~8

EDLP12  //learn edid from port 1 to source 2

>>  EDLD?*				// Learn EDID from Default Value ? to source *

?: Default Edid value 1~8

*: Input. 1~8

>> FSET

Factory reset

>>IRL*   // Send IR command from Receiver to Main board control  unit

*: 1: enable IR from Receiver to Main board decoder

0: disable IR from Receiver to Main board decoder

Default value is disable.

Software command[Hex mode]

len 0x4d 0x41 0x52 0x88 0x43 0x48 0xff cmd cm1 cm2 cm3 cm4 cm5 cm6 cm7 … cm* checksum

len is the length from len to checksum

cmd is command index

cm1 to cm* is  setting value

checksum = sum from len to cm*

example:

set output mapping

0x12 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x02 0x01 0x01 0x01 0x01 0x01 0x01 0x01 0x01 0xe

Cmd = 2 for set port mapping

Port1 1 port 2 1 port3 1 port4 1 port5 1 port6 1 port7 1 port8 1

Check sum 0x0e

Echo 0xaa

1.>

Cmd =0  power on or idle

0x0b 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x00 cm1 checksum

Cmd1: 0x55  idle 0xaa power on

2.>

Cmd =1  get port mapping

0x0a 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x01 0xfd

Echo :

0xaa  0x13 p1 p2 p3 p4 p5 p6 p7 p8 s1 s2 s3 s4 s5 s6

s7 s8 pwd checksum

0xaa is the echo for receive command

0x13 is the data length [from p1 to checksum]

p1~p8 is the port mapping. 1~8 or 0[port off]

s1~s8 is the source status. 1: source exist 0: source off

pwd is the matrix status. 1: power on. 0: idle

example

0xaa 0x13 0x01 0x02 0x03 0x04 0x05 0x06 0x07 0x08 0x00 0x00 0x00 0x00 0x00 0x00 0x00 0x00 0x01 0x38

3.>

Cmd = 2 for set port mapping

0x12 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x02 Port1 1 port 2 1 port3 1 port4 1 port5 1 port6 1 port7 1 port8 + checksum

Port1~port8: source value from 1~8

0x80+source for close output port.

Ex 0x81 port select source 1 but set close.

Echo 0xaa

If the port value is the same, the output port will keep the video.

Add 0x10 to source. The output port will re trigger (including off/on and do hdcp)

For example:

Now port1 select source 1

Port1 = 0x01 : video not change

Port1 = 0x01 : video turn off/on and do hdcp again.

4.>

Cmd =5  get firmware version

0x0a 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x05 0x01

5.>

Cmd =10  read edid from output port

0x0b 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x0a cm1 + checksum

Cm1: port number 1~8

Echo:

Read ok :0xaa + 256 byte hex value.

Read fail: 0x55.

6.>

Cmd =11  read edid from input

0x0b 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x0b cm1 + checksum

Cm1: input number 1~8

Echo:

Read ok :0xaa + 256 byte hex value.

Read fail: 0x55.

7.>

Cmd =12  edid learning from cm2 to cm3

0x0c 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x0c cm1 cm2 cm3 checksum

Cm1: input number 1~8

cm1: 0x03: read port edid and write to source

0x06: read default edid and write to source

cm2: input number:

1~8: input 1 to 8

0xf1: all input

Echo: 0xaa: OK  0x55 fail

Ex:

0x0c 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x0c 0x01 0xf1 0xfc

Read port1 edid and write to all input

7.>

Cmd =32  factory reset

0x0a 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x20 0x1c

8.>

Cmd =49  read IP and network informateion

0x0a 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x31 0x2d

Echo:

0xaa + 0x16 + ip1 ~ip4 mask1~4 gateway1~4 dns11~dns14 dns21~dns22  sumvalue

9.>

Cmd= 50 wirte ip,maskvalue,gateway,dns1,dns2

0x22 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x32 ip1 ~ip4 mask1~4 gateway1~4 dns11~dns14 dns21~dns22 checksum

Ex: ip1~4= 192.168.1.14

ip1=192

ip2=168

ip3=1

ip4=14

mask1~4 = 255.255.255.0

mask 1=255

mask 2=255

mask 3=255

mask 4=0

10.>

Cmd= 80 save the I/O mapping to mapping memory

0x0b 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x50 cm1 checksum

cm1: group number

0x0b 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x50 0x01 0x4e

Save the input/output mapping to group 1.

11.>

Cmd= 81 load the I/O mapping from mapping memory and change I/O mapping.

0x0b 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x51 cm1 checksum

cm1: group number

0x0b 0x4d 0x41 0x52 0x88 0x43 0x48 0xff 0x51 0x01 0x4e

Load the input/output mapping to group 1.

Group 1 memory  all source are input 1

Now: mapping 12345678

After load group1. Mapping 11111111