HDTV Supply

HDTVEX410L HDTVEX810L HDTVEX610L

VGA splitter/extender

HDTV Supply, Inc.
3835-R East Thousand Oaks Blvd
Unit 295
Westlake Village, CA 91362
(800) 841-9238
(805) 277-1870 Direct
(805) 371-4070 FAX - General
(805) 435-2623 FAX for orders, RMA info and availability
WEB: www.HDTVSupply.com
EMAIL: support @ NOSPAMhdtvsupply.com - delete NOSPAM and compress
MOBILE FRIENDLY: Mobile Friendly page

Features

• Sharpest and clearest VGA of any manufacturer

• Broadcast real-time VGA video or audio/video to multiple display locations

• Stereo audio can be broadcast to self-powered stereo speakers at the local unit and each remote location

• Easily expandable. Add remote units as you add monitors

• A pure hardware solution-no software conflicts

• Supports high-resolution video (1280x1024) at distances up to 300 meters

Higher resolutions can be achieved at shorter distances

• Built-in surge protection

Connection Diagram：

Specifications

| Connect with PC | One High Density DB15 Male; One 3.5mm female stereo audio jack |
| --- | --- |
| Video Input Frequency Ranges | Horizontal: 15 KHz to 130 KHz. Vertical: 30 Hz to 150 Hz |
| Audio Frequency Response | 20 Hz to 20 kHz, +/- 1 dB |
| Input Impedance | 75 Ohms |
| Audio Input Impedance | 10k Ohms |
| Local Video and Audio | One High Density DB15 Female; One 3.5mm female stereo audio jack |
| Connect with Remote | HDTVEX410L : 4 RJ45 HDTVEX810L : 8 RJ45 HDTVEX1610L : 16 RJ45 |
| Cable Type | Category 5/5e/6 UTP |
| Power Adapter | DC 12V/1A |
| LEDs | One for power, one for Video |
| Dimensions | HDTVEX410L :205X76X29mm HDTVEX810L :438X82X32mm HDTVEX1610L :438X82X32mm |